## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Introduction and Instruction Set Architectures (ISA)
Instructor: Siddharth Garg

## Slide 2: Logistics
Lectures
  Quizzes/exercises to keep you involved (bring your laptops!)
  15 minute break to keep you refreshed
Office hours
  Fridays 1PM-3PM
  2 Metrotech, 10.076
TAs
  Team of 4 TAs. Names and office hours will be announced soon.
TA Office Hours
Kang Li: 10AM-Noon Mondays
Rafael Jin: 10AM-Noon Wednesdays
2 MTC, 10.073 (CCS Lab)

## Slide 3: Grading (HWs and Labs)
3 Homeworks (20% of your final grade)
3 programming labs (20% of your final grade)
HWs and programming must be done individually
  Plagiarism policy applies
  DO NOT COPY HW ASSIGNMENTS OR CODE --- IMMEDIATE GRADE REDUCTION ON CLASS

## Slide 4: Grading (Midterm and Final)
Midterm scheduled for Oct. 27th during the Friday class hour (25% of total grade)
  Location will be announced later
Final exam review lecture scheduled for Dec. 14th during Thursday class hours
Final exam scheduled for Dec. 15th during Friday class hours (35% of total grade)
  Location will be announced later

## Slide 5: Plagiarism
Don’t do it
Don’t do it
Don’t do it
Don’t do it
Don’t do it
Don’t do it
Don’t do it
Don’t do it
Why not?
  You won’t learn much
  You’ll likely get caught
What happens if I get caught?
  Automatic zero on assignment and grade reduction
  Second strike and you fail the class

## Slide 6: Introduction
Algorithm
Problem-oriented Programming Language
Assembly Language
Micro-architecture
Digital Logic/Hardware
Examples: C/C++, Java, Python etc.
Step-by-step set of operations to solve a certain problem
Step-by-step instructions that your computer can understand!
Instruction Set Architecture (ISA)
Examples: …….?
Hardware-level description of how processor executes ISA
Many different ways of executing the same ISA
Examples: …….?
Compiler
Boolean logic gates, flip-flops/registers
Computer Architecture

## Slide 7: Historical Perspective: Harvard Mark I
60 “constant registers” (23 decimals + sign)
  Manually programmed constants
72 “storage counters” (23 decimals + sign)
  To hold intermediate results of computation
Instruction Format
  24-bits
  Fed with punch card
“Harvard Architecture” - separate memory for instructions and data
OUT (operand) | IN (operand, result stored here) | MISC. (which operation is performed)
Storage Counter 1 (Decimal Code: 1) | Storage Counter 2 (Decimal Code: 2) | SUB (Decimal Code: 32)
No branch instructions!

## Slide 8: EDVAC: Electronic Discrete Variable Automatic Computer
Internal magnetic “tape” based memory consisting of 1024 44-bit words
  Digital (0,1) instead of decimal (0,1,2,..9) representation
  Each word could represent either data or an instruction
  Up to 16 different instructions, including branch instructions
Von Neumann Architecture: Unified memory for data and instructions
Op Code (4 bits) | OP 1 (10 bits) | OP 2 (10 bits) | OP 3 (10 bits) | Next Instruction
Which operation (add, sub, mult, branch…) | Address of 1st operand | Address of 2nd operands | Address where result stored | Address from where next instruction fetched

## Slide 9: Harvard Vs. Von Neumann Architecture
Central Processing Unit (CPU)
Data + Instruction Memory
Central Processing Unit (CPU)
Data Memory
Inst. Memory
Memory must be a RAM (random access memory) with read/write capability
Data memory must be a RAM (random access memory) with read/write capability
Instruction memory can be a ROM (read only memory)
Harvard
Von Neumann

## Slide 10: Harvard Vs. Von Neumann: Pros/Cons
Harvard Architecture
  Con: dedicated memory for code results in inefficient use of memory capacity
  Pro: Code memory can be read only (faster, smaller, cheaper)
  Pro: code is protected
Von Neumann Architecture
  Pro: flexible use of available memory capacity
  Con: Memory needs to support read/write
  Con: code can be maliciously re-written
Discuss: Pros vs cons of Harvard vs. Von Neumann architecture
Notes: Dedicated code memory wastes space, self-modifying code; security analysis; faster Rom

## Slide 11: Invention of the Transistor
Vacuum tubes ruled in first half of 20th century Large, expensive, power-hungry, unreliable
1947: first solid-state transistor
  John Bardeen and Walter Brattain at Bell Labs
AT&T Archives. Reprinted with permission.
ENIAC had 18000 vacuum tubes and consumed 150 kW of power

## Slide 12: From Transistors to Integrated Circuits
1958: First integrated circuit
  Flip-flop using two transistors
  Built by Jack Kilby at Texas Instruments
2010
  Intel Core i7 mprocessor
    2.3 billion transistors
  64 Gb Flash memory
    > 16 billion transistors
Courtesy Texas Instruments
[Trinh09]
© 2009 IEEE

## Slide 13: Moore’s Law: Then
1965: Gordon Moore plotted transistor on each chip
  Fit straight line on semilog scale
  Transistor counts have doubled every 26 months
Integration Levels
SSI: 10 gates
MSI: 1000 gates
LSI: 10,000 gates
VLSI: > 10k gates
[Moore65]
Electronics Magazine

## Slide 14: And Now…

## Slide 15: Feature Size
Minimum feature size shrinking 30% every 2-3 years

## Slide 16: Corollaries
Many other factors grow exponentially
  Ex: clock frequency and therefore processor performance

## Slide 17: Metrics of Performance
Compiler
Programming
Language
Application
Datapath
Control
Transistors
Wires
Pins
ISA
Function Units
(millions) of Instructions per second: MIPS
(millions) of (FP) operations per second: MFLOP/s
Cycles per second (clock rate)
Megabytes per second
Answers per month
Operations per second

## Slide 18: Modern Computers
CPU PC, registers, Datapath, control path, unified main memory, caches, Disk, I/O
PC
Central Processing Unit (CPU)
Instructions are in processed sequentially (one after the other). Address of current instruction stored in Program counter (PC)
+
X
Datapath
Main Memory
Control
Path
Fast local access to data. Based on idea of temporal locality: frequent reuse of data fetched from memory
Register File
Reg. 1
Reg. 2
Reg. M
Memory Controller
Adders, multipliers etc.
Unified: stores both instructions and data
Random access: CPU can read/write any byte of data
Handles read/write requests from CPU to main memory
byte 1
byte 2
byte N
Array of Bytes

## Slide 19: Role of the ISA
Instruction Set Architecture (ISA) serves as a contract between programmer and hardware
  Functional description of storage locations and the operations it can perform
Storage locations:
  Registers: typically a small number of registers. Ex: MIPS ISA defines 32 32-bit registers.
  Memory: much larger, but off-chip and higher access cost. MIPS ISA has a 32-bit memory address, so in theory 232 Bytes = 4GB of data.
Operations:
  Integer Add, Integer Multiply, Branch, FP Add, FP Multiply, FP Divide

## Slide 20: Role of the Micro-architecture
The micro-architecture is responsible for faithfully executing programs written using the ISA
  Same ISA can have multiple different micro-architectural implementations with different performance and power consumption
PC
+
X
Datapath
Control
Path
Register File
Reg. 1
Reg. 2
Reg. M
Memory Controller
+
2 Adders even though instructions are processed sequentially
+
+
add r3, r1, r2
add r6, r5, r4
r1
r2
r3
r4
r6
r6
More area/power but
higher performance!
(Identical functionality)

## Slide 21: Role of the Micro-architecture
Cache is managed entirely by hardware
Programmer and oblivious to its existence
PC
+
X
Datapath
Main Memory
Control
Path
Register File
Reg. 1
Reg. 2
Reg. M
Memory Controller
byte 1
byte 2
byte N
Array of Bytes
+
On-chip copy of main memory contents
Cache

## Slide 22: Role of the Micro-architecture
Hardware/OS managed virtual memory provides the appearance of a 4GB contiguous address space
PC
+
X
Datapath
Main Memory
Control
Path
Register File
Reg. 1
Reg. 2
Reg. M
Memory Controller
byte 1
byte 2
byte N
Array of Bytes
+
On-chip copy of main memory contents
Cache
32-bit PC implies 4GB of addressable memory
Actual main memory capacity can be <4 GB
Hard Disk

## Slide 23: ISAs are Abundant
x86
x86-64
IA64
x86
x86-64 (AMD64)
T32 (Thumb)
A32 (ARM)
A64 (ARM-64)
PowerPC
MIPS32
MIPS64
VAX
SPARC
CISC
ISAs
RISC ISAs
Alpha
IBM360
Laptop
Desktop
Laptop
Desktop
Servers
Servers
Mobile
Servers
Laptop
Desktop
Embedded

## Slide 24: ISA Design: Instruction Length
An instruction is a basic unit of an ISA
Fixed versus variable length instructions
  Fixed: Each instruction in the MIPS ISA is 32 bits (4 Bytes) long
  Variable: x86 instructions vary from 1 to 17 Bytes long
32 bits
8 bits
136 bits
Typical of RISC ISAs
Typical of CISC ISAs
Trade-offs?
Notes: Imagine a book written without spaces. Would it be useful if each word had the same length?

## Slide 25: ISA Design: Operand Addresses
ALU
(+, -, x)
Where do the operands come from?
Where is the result written?
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Instruction specifies 2 source and 1 destination register
“3-Address” ISA (E.g., MIPS ISA)
add rs, rt, rd
($rd ←$rs + $rt)
Value of register rt
sub rs, rt, rd
($rd ←$rs - $rt)

## Slide 26: Example: Swap Using Add/Sub
Swap the contents of Reg. 2 (r2) and Reg. 3 (r3) using only add and sub operations
X = X + Y;
Y = X – Y; //X +Y – Y = X
X = X - Y ; //X +Y – X = Y
There are simpler ways to implement a swap in the MIPS ISA!
add r2, r3, r2
sub r2, r3, r3
sub r2, r3, r2
X
Y
r2
r3
X+Y
Y
r2
r3
X + Y
X
r2
r3
Y
X
r2
r3

## Slide 27: 1- and 2-Address ISAs
Write result back to a source register
“2-Address” ISA
(Have we seen an example today?)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Special purpose “Accumulator” serves as an operand and as the destination
“1-Address” ISA
(Also called an “Accumulator Architecture”)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator

## Slide 28: Swap Routine for 2-Address ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
add rs, rd
($rd ←$rd + $rs)
sub rs, rd
($rd ←$rd - $rs)
X = X + Y;
Y = X – Y; //X +Y – Y = X
X = X - Y ; //X +Y – X = Y
X is stored in r2
Y is stored in r3
Assume r4 can be used as temp
add r3, r2 //r2 = X+Y
sub r2, r3 //r3=-X
add r3, r2 //r2=Y
sub r4, r4 //r4=0
sub r3, r4 // r4=X
sub r3,r3 //r3=0
add r4,r3 //r3=X

## Slide 29: Swap Routine for 1-Address ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
add rs
($acc ←$acc + $rs)
sub rs
($acc ←$acc - $rs)
mvto rs
($rs ←$acc )
mvfrm rs
($acc ←$rs)
X = X + Y;
Y = X – Y; //X +Y – Y = X
X = X - Y ; //X +Y – X = Y
X is stored in r2
Y is stored in r3
Assume r4 can be used as temp
mvfrm r2 //acc=X
add r3 //acc=X+Y
mvto r2 //r2=X+Y
sub r3 //acc = X
mvto r3 //r3 = X
mvfrm r2 //acc=X+Y
sub r3 //acc = Y
mvto r2 //r2=Y

## Slide 30: So Which is “Better”?
Metrics?
  Code size (Bytes)
  Design complexity
add r2, r3, r2
sub r2, r3, r3
sub r2, r3, r2
add r3, r2
sub r4, r4
add r4, r3
sub r3, r4
sub r3, r4
add r3, r2
sub r2, r3
mvfrm r2
add r3
mvto r2
sub r3
mvto r3
mvfrm r2
sub r3
mvto r2
Assume 5-bit opcode for all 3 ISAs
How many bits requires to address 32 registers?
Code size = Num Insts x Bits/Inst
  3-Address ISA
  2-Address ISA
  1-Address ISA

## Slide 31: So Which is “Better”?
Metrics?
  Code size (Bytes)
  Design complexity
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
2 Read ports
1 Write port
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
1 Read port
1 Write port
1 R/W accum

## Slide 32: 0-Address ISA (Stack Machines)
STACK
TOS
ALU
(+, -, x)
Accumulator
pop M
Mem[M] ← $TOS
TOS ← TOS-1
push M
TOS ← TOS+1
$TOS ← Mem[M]
byte 1
byte 2
byte N
Array of Bytes
Main Memory
add
$TOS-1 ←$TOS + $(TOS-1)
TOS ←TOS-1

## Slide 33: How is Memory Accessed
Can also be bit-addressable, 32-bit addressable, 64-bit addressable, etc.
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
Addr
Mem[Addr]
“Byte addressable”
How many bits should Addr have?
{Mem[Addr], Mem[Addr+1], Mem[Addr+2], Mem[Addr+3]}

## Slide 34: Load-Store ISA
Instructions like add, sub etc. operate only on registers (examples: MIPS, ARM, 3/2/1/0-Address ISAs we have seen so far)
  Separate Load/Store instructions to fetch data from memory into registers and to write data back from registers to memory
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
add rs, rt, rd
($rd ←$rs + $rt)
load rt, M
($rt ←Mem[M])
store rt, M
( Mem[M] ←$rt )
Load data at memory location M
into register rt
Store data in register rt to memory location M

## Slide 35: Memory-Memory ISA
Allow instructions like add/sub to operate directly on data in memory (Examples include: x86, VAX etc.)
Most generally, each of the two operands and the result can be read-from/written-to either memory or register file
  Pros?
  Cons?
add Ms, Mt, Md
(Mem[Md] ←Mem[Ms] + Mem[Mt])
Memory address

## Slide 36: Addressing Modes
How to specify where to read from/write to
Orthogonal ISA: each op supports every addressing mode (ex: VAX)
load rt, M
($rt ←Mem[M])
Absolute
load rs, rt
($rt ←Mem[$rs])
Register Indirect
load rs, rt, offset
($rt ←Mem[offset+$rs])
Displaced/Based
Directly provide memory address
Memory address from register rs
Add an offset to address stored in register rs
load rs, rt, rd
($rd ←Mem[$rs + $rt])
Indexed
load rt, rs
($rt ←Mem[Mem[$rs]]
Memory Indirect
load rt, rs
($rt ←Mem[$rs]
$rs ←$rs + 1)
Auto-increment
Base memory address and offset from registers
Use value at Mem[$rs] as address
Same as Register indirect + value in rs is automatically incremented

## Slide 37: What Makes a Good ISA
Ease of hardware implementations
  Decoder for fixed vs. variable instruction lengths
  Simple vs. complex addressing modes
Ease of software implementation
  Can the programmer/compiler use the ISA easily?
  How many assembly instructions to represent a single line of code in a high-level language? “semantic gap”
Backwards compatibility
  ISA will have to be supported into the future; new instructions can be added but existing instructions cannot be removed

## Slide 38: CISC Vs. RISC
CISC: “Complex” Instruction Set Computer
RISC: “Reduced” Instruction Set Computer
  Each CISC instruction = multiple RISC instructions
CISC vs. RISC debate dominated the 80s/early 90s but is largely resolved now
  CISC ISAs like x86 are “broken down” internally into simpler RISC-like instructions (microcode)
  x86 is “externally CISC but internally RISC”
  Other popular ISAs like ARM and MIPS are RISC

## Slide 39: ISA Comparison
 | VAX | x86 | MIPS
ISA Type | CISC | CISC (but internally RISC) | RISC
Instruction Length | Variable | Variable | Fixed
Addressing Modes | 3-Address; memory-memory; orthogonal addressing modes | 2-Address; register-memory | 3-Address; load/store ISA