## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Introduction and Instruction Set Architectures (ISA)
Instructor: Siddharth Garg

## Slide 2: ISA Design: Operand Addresses
ALU
(+, -, x)
Where do the operands come from?
Where is the result written?
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Instruction specifies 2 source and 1 destination register
“3-Address” ISA (E.g., MIPS ISA)
add rs, rt, rd
($rd ←$rs + $rt)
Value of register rt
sub rs, rt, rd
($rd ←$rs - $rt)

## Slide 3: 1- and 2-Address ISAs
Write result back to a source register
“2-Address” ISA
(Have we seen an example today?)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Special purpose “Accumulator” serves as an operand and as the destination
“1-Address” ISA
(Also called an “Accumulator Architecture”)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator

## Slide 4: So Which is “Better”?
Metrics?
  Code size (Bytes)
  Design complexity
add r2, r3, r2
sub r2, r3, r3
sub r2, r3, r2
add r3, r2
sub r4, r4
add r4, r3
sub r3, r4
sub r3, r4
add r3, r2
sub r2, r3
mvfrm r2
add r3
mvto r2
sub r3
mvto r3
mvfrm r2
sub r3
mvto r2
Assume 5-bit opcode for all 3 ISAs
How many bits requires to address 32 registers?
Code size = Num Insts x Bits/Inst
  3-Address ISA
  2-Address ISA
  1-Address ISA

## Slide 5: So Which is “Better”?
Metrics?
  Code size (Bytes)
  Design complexity
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
2 Read ports
1 Write port
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
1 Read ports
+ 1 R/W accum

## Slide 6: How is Memory Accessed
Memory can also be bit-addressable, 32-bit addressable, 64-bit addressable, etc.
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
Addr
Mem[Addr]
“Byte addressable”
How many bits should Addr have?
{Mem[Addr], Mem[Addr+1], Mem[Addr+2], Mem[Addr+3]}

## Slide 7: Little/Big Endian
byte 1
byte 2
Main Memory
Addr=1000
{2FAA019C}
or
{9C01AA2F}
1000
1001
1002
1003
2F
AA
01
9C
Assuming an instruction or data word is 32 bits of data from locations [Addr,Addr+3] are fetched from Main Memory.
Big Endian: Data = {Mem[Addr], Mem[Addr+1], Mem[Addr+2], Mem[Addr+3]}
  Examples: IBM360
Little Endian: Data = {Mem[Addr+3], Mem[Addr+2], Mem[Addr+1], Mem[Addr]}
  Examples: x86, x86-64, AMD64
Bi-Endian: both supported! (Ex: MIPS)
From CPU
To CPU
Address

## Slide 8: Load-Store ISA
Instructions like add, sub etc. operate only on registers (examples: MIPS, ARM, 3/2/1/0-Address ISAs we have seen so far)
  Separate Load/Store instructions to fetch data from memory into registers and to write data back from registers to memory
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
add rs, rt, rd
($rd ←$rs + $rt)
load rt, M
($rt ←Mem[M])
store rt, M
( Mem[M] ←$rt )
Load data at memory location M
into register rt
Store data in register rt to memory location M

## Slide 9: Memory-Memory ISA
Allow instructions like add/sub to operate directly on data in memory (Examples include: x86, VAX etc.)
Most generally, each of the two operands and the result can be read-from/written-to either memory or register file
  Pros?
  Cons?
add Ms, Mt, Md
(Mem[Md] ←Mem[Ms] + Mem[Mt])
Memory address

## Slide 10: Addressing Modes
How to specify where to read from/write to
Orthogonal ISA: each op supports every addressing mode (ex: VAX)
load rt, M
($rt ←Mem[M])
Absolute
load rs, rt
($rt ←Mem[$rs])
Register Indirect
load rs, rt, offset
($rt ←Mem[offset+$rs])
Displaced/Based
Directly provide memory address
Memory address from register rs
Add an offset to address stored in register rs
load rs, rt, rd
($rd ←Mem[$rs + $rt])
Indexed
load rt, rs
($rt ←Mem[Mem[$rs]]
Memory Indirect
load rt, rs
($rt ←Mem[$rs]
$rs ←$rs + 1)
Auto-increment
Base memory address and offset from registers
Use value at Mem[$rs] as address
Same as Register indirect + value in rs is automatically incremented

## Slide 11: Addressing Modes
load rt, M
($rt ←Mem[M])
Absolute
load rs, rt
($rt ←Mem[$rs])
Register Indirect
load rs, rt, offset
($rt ←Mem[offset+$rs])
Displaced/Based
32-bit instruction
cannot store a 32-bit address
load rs, rt, rd
($rd ←Mem[$rs + $rt])
Indexed
load rt, rs
($rt ←Mem[Mem[$rs]]
Memory Indirect
load rt, rs
($rt ←Mem[$rs]
$rs ←$rs + 1)
Auto-increment
Data is frequently stored relative to a base location
Pointers
Emulate absolute addressing (more later)
Pointer to a pointer!
Array accesses
(rs stores pointer to an array)

## Slide 12: What Makes a Good ISA
Ease of hardware implementations
  Decoder for fixed vs. variable instruction lengths
  Simple vs. complex addressing modes
Ease of software implementation
  Can the programmer/compiler use the ISA easily?
  How many assembly instructions to represent a single line of code in a high-level language? “semantic gap”
Backwards compatibility
  ISA will have to be supported into the future; new instructions can be added but existing instructions cannot be removed

## Slide 13: CISC Vs. RISC
CISC: “Complex” Instruction Set Computer
RISC: “Reduced” Instruction Set Computer
  Each CISC instruction = multiple RISC instructions
CISC vs. RISC debate dominated the 80s/early 90s but is largely resolved now
  CISC ISAs like x86 are “broken down” internally into simpler RISC-like instructions (microcode)
  x86 is “externally CISC but internally RISC”
  Other popular ISAs like ARM and MIPS are RISC

## Slide 14: ISA Comparison
 | VAX | x86 | MIPS
ISA Type | CISC | CISC (but internally RISC) | RISC
Instruction Length | Variable | Variable | Fixed (32 bits)
Addressing Modes | 3-Address Memory-memory Orthogonal addressing modes | 2-address Register-memory | 3-Address Load/store ISA

## Slide 15: In-Class Problem 1
We will explore the advantages of
  The auto-increment addressing mode
  Orthogonal ISA
addr[A]
ALU
(+, -, x)
Accumulator
Main Memory
A[0]
A[1]
A[N-1]
r1
r2
sum
add rs
($acc ←$acc + $rs)
addinc rs, rt
($acc ←$acc + Mem[$rs + $rt]
$rs ←$rs + 1)
ble rs, imm, addr
(if ($rs<=imm)
goto addr)
r0
0
Write code to sum the array and store the sum in register r2.
mvto rs
($rs ←$acc )
mvfrm rs
($acc ←$rs)

## Slide 16: In-Class Problem 1
We will explore the advantages of
  The auto-increment addressing mode
  Orthogonal ISA
addr[A]
ALU
(+, -, x)
Accumulator
Main Memory
A[0]
A[1]
A[N-1]
r1
r2
sum
mvfrm r0
L: addinc r0, r1
ble r0, N-1, L
mvto r2
r0
0

## Slide 17: MIPS ISA Overview
32-bit ISA (what does this mean?)
  Instruction length: 32 bits
  Data word length: 32 bits
32 general purpose registers ($0, $1, $2, … $31); 32-bits each
  Register $0 is hard-wired to 0 (constant)
  All other registers can be used as read/write
  But, certain registers dedicated for specific purposes by compiler
    Global pointer ($28), Stack pointer ($29), Frame pointer ($30), Return Address ($31)
    We wont worry about these conventions in this class!
Two dedicated 32-bit registers hi and lo for multiplication ops
Separate regs/unit for floating point ops (discussed later)

## Slide 18: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rt]; signed addition; trap on overflow
sub rs, rt, rd // R[rd] ← R[rs] - R[rt]; signed subtraction; trap on overflow
or rs, rt, rd // R[rd] ← R[rs] | R[rt]; bit-wise Boolean OR operation
sll rt, rd, shamt // R[rd] ← R[rt] << shamt; logical shift left
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Add: 100000 = 20hex
Sub: 100010 = 22hex
Or: 100101 = 25hex
Sll: 000000 = 00hex

## Slide 19: MIPS R-type Instructions: Add vs Addu
add rs, rt, rd // R[rd] ← R[rs] + R[rt]; signed addition; trap on overflow
rs, rt and rd are assumed to contain 32-bit signed, 2’s complement numbers
  MSB (32nd bit) indicates if the number is positive or negative
  Review 2’s complement representation (https://en.wikipedia.org/wiki/Two%27s_complement)
Example: assume only 4-bit numbers in range [-8,7]
rs = 0101 (5)
rt =+ 0110 (6)
rd= 1011 (-4)  Overflow!
addu rs, rt, rd // R[rd] ← R[rs] + R[rt];
NO trap on overflow

## Slide 20: MIPS R-type Instructions: Mult
mult rs, rt // {hi,lo} ← R[rs] * R[rt]; signed multiplication
hi and lo are two special purpose 32-bit registers that store the result of a multiplication operation
  Why? Multiplication result of two 32-bit values needs at least 64 bits
What does this remind you of?
mvhi rd //R[rd] ← R[hi]
mvlo rd //R[rd] ← R[lo]
32-bits
rs
rd
X
32-bits
64-bits
{hi (upper 32-bits) , lo (lower 32-bits)}

## Slide 21: MIPS Instructions: I-Type
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
beq rs, rt, imm // if{R[rs] == R[rt]} branch to PC + 4 + BranchAddress; (“PC relative”)
//BranchAddress = {signextendimm,imm[15:0],00}
ori rs, rt, imm // R[rt] ← R[rs] | {ZeroExtend,imm}; bit-wise Boolean OR operation
lw rs, rt, imm // R[rt] ← Mem[ {SignExtendimm} + R[rs] ] (“Displaced/based”)
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0
Operand register
Immediate operand
addi: 8hex
beq: 4hex
ori: 25hex
lw: 23hex
Result register
(“PC relative”)

## Slide 22: MIPS Instructions: J-Type
j address // PC ← JumpAddress
jal address // R[31] ← PC+8; PC ← Jumpaddress;
//JumpAddress = { PC+4[31:28], address, 2’b0 }
// Also, R-type jump
jr rs // PC ← R[rs]
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex

## Slide 23: Implementation of the MIPS ISA
Hardware building blocks
PC
Program Counter
A 32-bit “register”
(can store information)
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
Register File
32 32-bit registers
(2 Read ports, 1 Write Port)
5 bit address
5 bit address
5 bit address
32 bit data
32 bit data
32 bit data
Set to ‘1’ to enable write
result
ALU op
? bits
oprnd1
oprnd2
32 bits
32 bits
32 bits
Add: 20hex
Addu: 21hex
Sub: 23hex
Subu: 24hex
And: 25hex
Or: 24hx
Nor: 27hex
Arithmetic/Logic Unit (ALU)

## Slide 24: Implementation of the MIPS ISA
Hardware building blocks
Is this a von Neumann architecture?
Read Address
Instruction
Instruction Memory
(Read only)
32 bits
32 bits
Address
Write
Data
Read Data
Data Memory
Read Mem
Write Mem
32 bits
32 bits
32 bits
Set to ‘1’ to enable read; 0 otherwise
Set to ‘1’ to enable write; 0 otherwise
Data Memory
(Either read or write, but not both together)

## Slide 25
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
R-Type ALU Instructions

## Slide 26
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
I-Type ALU Instructions
20:16
Sign
Extend
15:0
32
Rs

## Slide 27
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
15:11
Adder
+4
ALU op
3
Wrt Enable
1
Combined R-Type and
I-Type ALU Instructions
20:16
Sign
Extend
15:0
MUX
a
b
control
a:b?control
I-Type?
I-Type?

## Slide 28
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
Read Mem
Write Mem

## Slide 29
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
IsLoad?
0

## Slide 30
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Store
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Did we miss something?
0

## Slide 31
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
I-Type Store
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
!IsStore?