## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Single Cycle MIPS Implementation
Instructor: Siddharth Garg

## Slide 2: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rd]; signed addition; trap on overflow
sub rs, rt, rd // R[rd] ← R[rs] - R[rt]; signed subtraction; trap on overflow
or rs, rt, rd // R[rd] ← R[rs] | R[rt]; bit-wise Boolean OR operation
sll rt, rd, shamt // R[rd] ← R[rt] << shamt; logical shift left
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Add: 100000 = 20hex
Sub: 100010 = 22hex
Or: 100101 = 25hex
Sll: 000000 = 00hex

## Slide 3: MIPS Instructions: I-Type
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
beq rs, rt, imm // if{R[rs] == R[rt]} branch to PC + 4 + Target; (“PC relative”)
ori rs, rt, imm // R[rt] ← R[rs] | {ZeroExtend,imm}; bit-wise Boolean OR operation
lw rs, rt, imm // R[rt] ← Mem[ {SignExtendimm} + R[rs] ] (“Displaced/based”)
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0
Operand register
Immediate operand
addi: 8hex
beq: 4hex
ori: 25hex
lw: 23hex
Result register
(“PC relative”)

## Slide 4: MIPS Instructions: J-Type
j address // PC ← {PC+4[31:28], address, 00}
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex

## Slide 5: Implementation of the MIPS ISA
Hardware building blocks
PC
Program Counter
A 32-bit “register”
(can store information)
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
Register File
32 32-bit registers
(2 Read ports, 1 Write Port)
5 bit address
5 bit address
5 bit address
32 bit data
32 bit data
32 bit data
Set to ‘1’ to enable write
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
.
.
00000
00001
00010
00011
11111
A21F FFB3
0000 0000
BB33 CD53
1242 221E
0001 0001
ADDRESS
DATA
00001
11111
0
A21F FFB3
0001 0001
FFFF FFFF
00010
1
FFFF FFFF
00010
FFFF FFFF

## Slide 6: Arithmetic Logic Unit
result
ALU op
? bits
oprnd1
oprnd2
32 bits
32 bits
32 bits
Add: 20hex
Addu: 21hex
Sub: 22hex
Subu: 23hex
And: 24hex
Or: 25hx
Nor: 27hex
Arithmetic/Logic Unit (ALU)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Inst[2:0] decides which operation the ALU performs.
3
In-Class Problem 1: how do we set the bits of ALUop?
NOTE: Updated funct values

## Slide 7: Implementation of the MIPS ISA
Hardware building blocks
Is this a von Neumann architecture?
Read Address
Instruction
Instruction Memory
(Read only)
32 bits
32 bits
Address
Write
Data
Read Data
Data Memory
Read Mem
Write Mem
32 bits
32 bits
32 bits
Set to ‘1’ to enable read; 0 otherwise
Set to ‘1’ to enable write; 0 otherwise
Data Memory
(Either read or write, but not both together)

## Slide 8
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
R-Type ALU Instructions
“Datapath”

## Slide 9
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
Example: Instruction at PC=0
000000
00001
.
.
00000
00001
00010
00011
11111
A21F FFB3
0000 0000
BB33 CD53
1242 221E
0001 0001
RF Contents
00010
00011
00000
010100
00001
00010
00011
0
A21F FFB3
BB33 CD53
1
0
4
4
A21F FFB3 | BB33 CD53

## Slide 10
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
I-Type ALU Instructions
20:16
Sign
Extend
15:0
32

## Slide 11
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
15:11
Adder
+4
ALU op
3
Wrt Enable
1
Combined R-Type and
I-Type ALU Instructions
20:16
Sign
Extend
15:0
MUX
a
b
control
a if (control = 1)
b if (control = 0)
I-Type?
I-Type?

## Slide 12
ALU
result
ALU op
3
Combined R-Type and
I-Type ALU Instructions
What about ALUop?
Add: 20hex
Addu: 21hex
Sub: 22hex
Subu: 23hex
And: 24hex
Or: 25hx
Nor: 27hex
Addi: 8hex
Addiu: 9hex
Andi: chex
Ori: dhx
Function Field
OpCode
http://www-inst.eecs.berkeley.edu/~cs61c/resources/MIPS_Green_Sheet.pdf

## Slide 13
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = ?
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
Read Mem
Write Mem

## Slide 14
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
IsLoad?
0

## Slide 15
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Store Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
In-Class Problem 2:
Did we miss something?
0
sw rs, rt, imm //M[R[rs]+SignExtendimm] ← R[rt]

## Slide 16
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
!(IsStore?)
Final Data-Path
(Excluding Control Flow Instructions)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?

## Slide 17: Control Flow
J-Type Control Flow
  4 MSB bits taken from the 4 MSBs of PC+4
  Next 26 bits taken from the “address” field
  Last 2 bits are set to zero? (why?)
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
j address // PC ← {PC+4[31:28], address, 00}, opcode=2hex

## Slide 18
PC
Read Address
Instruction
Instruction Memory
Adder
+4
J-Type Control Instruction
RF Onwards Not Shown
Concat
31:28
PC+4
25:0
00
J-Type?
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
15:0
I-Type?
!(IsStore?)
What about WrtEnable?
0
!(J-Type?)

## Slide 19: Control Flow
I-Type Branch Instruction
  First 30 MSBs from sign extended immediate
  2 LSBs are always 0
beq rs, rt, imm // If (R[rs]==R[rt])
// PC ← PC + 4 + {SignExtendImm, 00},
// else
// PC ← PC + 4
// opcode=4hex
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0

## Slide 20
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
Sign
Extend
15:0
I-Type?
I-Type?
PC
Read Address
Instruction
Instruction Memory
Adder
+4
Concat
31:28
PC+4
25:0
00
NextPC? = function(J-Type?, IsBranch?, IsEq?)
Adder
PC+4
=
IsEq?
{SignExtendImm[29:0],00}
29:0
!(IsBranch?)
3:1 MUX

## Slide 21
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Generating Control Signals
(Control Path)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad?
IsStore?
I-Type?
Wrt Enable

## Slide 22
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad? = (Inst[31:26] == 100011)
IsStore? = (Inst[31:26] == 101011)
I-Type? = (Inst[31:26] != 00000) && (Inst[31:26] != 00010)
Wrt Enable

## Slide 23
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (Inst[31:26] == 100011) | (Inst[31:26] == 101011)
ALUop = 001
Else
ALUop = Inst[2:0]
ALUOp

## Slide 24
Control Path
Instruction Fetch Part Not Shown
If (Inst[31:26] == 100011) | (Inst[31:26] == 101011)
ALUop = 001
Else If (Inst[31:26]==000000)
ALUop = Inst[2:0]
Else
ALUop = Inst[28:26]

## Slide 25
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (IsStore? | IsBranch? | J-Type?)
WrtEnable = 0
Else
WrtEnable = 1
WrtEnable
J-Type? = (Inst[31:26]==000010)
IsBranch? = (Inst[31:26]==000100)

## Slide 26
If (IsBranch? && isEQ?)
NextPC? = 2
else if (J-Type?)
NextPC? = 1
else
NextPC? = 0
In-Class Problem 3:
Write pseudo-code for NextPC?

## Slide 27: Synchronous Implementation
Most digital circuits make use of a periodic “clock”
Flip-flop: basic component used in synchronous designs
  Looks at In at every positive clock edge and sets Out = In
  Holds the value of Out steady till next positive edge
FLIP-FLOP
clock
In
Out
Clock Period (seconds)
Positive Edge

## Slide 28: Flip-flop Operation
FLIP-FLOP
clock
In
Out
Clock
In
Out
0
1
0
0

## Slide 29: Synchronous Counter
FLIP-FLOP
clock
In
Out
Adder
+1
Clock
0
1
2
3
4
5
State is only updated at every positive clock edge
32 bits
32 bits

## Slide 30: Synchronous Single-Cycle MIPS
Goal: A new instruction is fetched and executed in every clock period
  For now let’s focus on the instruction fetch part of R-type instructions
PC
Read Address
Instruction
Instruction Memory
Adder
+4
Read Address
Instruction
Instruction Memory
Adder
+4
FLIP-FLOP
(PC)
CLOCK
PC register implemented using flip-flops

## Slide 31: Fetch Stage Operation
Read Address
Instruction
Instruction Memory
Adder
+4
FLIP-FLOP
(PC)
CLOCK
PC register implemented using flip-flops
Clock
0
4
8
PC
PC
Inst
nextPC
4
8
12
nextPC
In every clock cycle, the PC is updated and the corresponding instruction is fetched from instruction memory

## Slide 32: Execute/Write-Back Stage Operation
Goal: all updates to architectural state should occur at positive clock edges
  PC (already done!)
  Register file
  Data memory (not relevant for R-type instructions)

## Slide 33
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
0
add $1, $2, $3
3
12
15
4
4
15
.
.
00000
00001
00010
00011
11111
3
0
12
9
1
What’s wrong?

## Slide 34
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
0
add $1, $2, $3
3
12
15
4
4
15
.
.
00000
00001
00010
00011
11111
3
0
12
9
1
1
15
add $0, $1, $2
$3
$3
$2
$1
$2
$0
$1
1

## Slide 35
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
0
add $1, $2, $3
3
12
15
4
4
15
.
.
00000
00001
00010
00011
11111
3
0
12
9
1
1
add $3, $1, $2
$3
$3
$2
$1
$2
$3
$1
Simultaneous R/W request to the same register -> Write before Read
1
15
15

## Slide 36: Synchronous Counter Clock Period
FLIP-FLOP
clock
In
Out
Adder
+1
Clock
Assume each addition takes 1 ns. What is the minimum clock period?
32 bits
32 bits
5
5
1 ns
6
6
Period > 1ns

## Slide 37
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
0 ns
What is the clock period of the single cycle MIPS?
  Assume each block has a delay of 1 ns
1 ns
1 ns
2 ns
0 ns
0 ns
0 ns
2 ns
2 ns
3 ns
Minimum Period = 3 ns