## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Pipelined MIPS
Instructor: Siddharth Garg

## Slide 2: 5 Stage Pipeline (with support for load/store)
Basic steps in executing an R-type instruction
  Instruction fetch (IF)
  Instruction Decode/Register File Read (ID/RF)
  Execute in ALU (EX)
  Load result from or store result to data memory (MEM)
  Write-back Result to RF (WB)
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK

## Slide 3
IF
ID/RF
EX
MEM
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
lw $4 ,$5, imm
Read $1, $2
R[$1] + R[$2]
nop
Read $4
Addr=R[$4] + SgnImm
Load from Addr
WB
Write $3
WB
Write $5
t5
IF
ID/RF
EX
MEM
sw $6 ,$7, imm
Read $6, $7
Addr=R[$6] + SgnImm
Store R[$7]
to Addr
WB
Nop

## Slide 4: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5
EX-EX Forwarding (same as 4-stage pipeline)

## Slide 5: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5

## Slide 7: 5 Stage Pipeline (with support for load/store)
Two forwarding paths
  Same destination register in both forwarding paths? Pick data from EX-EX forwarding path
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction

## Slide 8: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
EX-EX Forwarding

## Slide 9: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4

## Slide 10: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Will this work?
Solution: Stall the pipeline

## Slide 11: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
ID/RF
MEM
add $4, $5, $6
Read $4, $5
nop
WB
Write $6
Solution: Stall the pipeline
EX
R[$4] + R[$5]
IF
IF
ID/RF
EX
MEM
Read $4, $5

## Slide 12: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding

## Slide 13: RAW Hazards: Load-Store Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
R[$4] = Mem[Addr]
WB
Write $4
IF
ID/RF
EX
MEM
sw $5, $4, imm
Read $5
Mem[Addr] = R[$4]
WB
Write $9
MEM->MEM Forwarding
Addr = R[$5] + SgnImm

## Slide 14: Branch Instructions
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
IF
Branch Taken/Not Taken not known till cycle T3!

## Slide 15: Solution 1: Stall+Flush
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
Fetch from PC+4 by default
IF
ID/RF
EX
MEM
WB
PC+4
IF
ID/RF
EX
MEM
WB
PC+8
Taken
NOP
NOP
NOP
NOP
NOP
NOP
NOP
IF
ADDR

## Slide 16: Reducing Stall Penalty
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
nop
WB
nop
IF
Move branch comparison and target address calculation to ID/RF
R[$3]==R[$4]?

## Slide 17: Solution 2: Moving Branch Calc to ID/RF Stage
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
Fetch from PC+4 by default
IF
ID/RF
EX
MEM
WB
PC+4
Taken
NOP
NOP
NOP
IF
ADDR
nop
nop

## Slide 18: What About RAW Dependencies?
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
nop
IF
ID/RF
EX
MEM
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
Result needed in ID/RF stage at the same time it is being computed

## Slide 19: What About RAW Dependencies?
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
nop
IF
ID/RF
EX
MEM
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
New EX->ID/RF Forwarding Path
ID/RF
Read $3, $4
R[$3]==R[$4]?

## Slide 20: Reducing Stall Penalty Further: Branch Delay Slot
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
IF
ISA specifies that the instruction following beq is always executed even if branch is Taken
R[$3]==R[$4]?
IF
PC+4
ADDR

## Slide 21: 5-Stage Pipeline
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Note: simplified pictures of IF and MEM stages
How are Imem and Dmem implemented?

## Slide 22: Memory System
ID/RF
(Decoder, RF)
EX
(ALU)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Memory Controller
Processor
Main Memory
Dynamic Random Access Memory (DRAM)
(Unified instruction and data memory)

## Slide 23: DRAM Details
ID/RF
(Decoder, RF)
EX
(ALU)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Memory Controller
3.6 GHz Pentium 4
Main Memory
Memory capacity: 4GB
Access Latency: 50 ns/word = ?? Clock cycles/word
= 50 ns / (1/3.6) ns = 180 cycles

## Slide 24: Memory Technologies
 | DRAM | SRAM (512 KB) | SRAM (4 MB)
Cell | 1 Transistor, 1 Capacitor (1T-1C) | 6 Transistor (6T) | 6 Transistor (6T)
Density (bits/um2) | High | Low | Low
Access Latency (ns) | Large | Small | Medium

## Slide 25: Memory Hierarchy
Decoder, RF, EX
SRAM
L1 Cache
SRAM
L2 Cache
CPU
DRAM Main Memory
Cache = “temporary storage space”
Instead of slow off-chip access to large DRAM, store frequently used data in on-chip SRAM cache
Hierarchy:
L1 Cache: small (32 KB), very fast (typically 1 clock cycle)
L2 Cache: larger (1 MB), slower (10s of nsecs)
L3 Cache: even larger ….
Main Memory: 4GB, 100s of nsecs

## Slide 26: Locality
Decoder, RF, EX
SRAM
L1 Cache
SRAM
L2 Cache
CPU
DRAM Main Memory
Temporal locality: if you’ve accessed some data, you’ll likely access it again in the near future
  Same instructions are repeatedly accessed within loops
  For example the loop counter
Spatial locality: if you’ve accessed some data, you’ll likely access nearby data
  Array accesses
  Instruction are accessed in sequential order

## Slide 27: Access Pattern Exhibiting Locality
http://www.eetimes.com/document.asp?doc_id=1275470

## Slide 28: Cache Organization
Caches store data in chunks of “cache blocks”
  Access to a cache returns an entire cache block
  A block can be as small as 1 byte, but can be larger (example: 4 bytes)
32 KB cache
1 Byte cache block
i.e., 32768 blocks
32 bit address
from CPU
Where does a block go when it is fetched into cache? (Placement)
How do we know if a block already exists in the cache? (Identification)
Which block should we kick out if there isn’t enough room? (Replacement)

## Slide 29: Direct Mapped Cache
Assume 32 KByte cache with a 1 Byte cache block
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
1 Byte = 8 bits

## Slide 30: Direct Mapped Cache: Placement
Each block in the cache has a log2(32768) = 15 bit “index”
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
Index
Index
(15 bits)
15 LSBs of address are used to look up (index) into the cache

## Slide 31: Direct Mapped Cache: Identification
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Addr 0
Addr 32768
0….00
0…………………….01
Addr ….
0….00
1…………………….11
Data Array
(8 bits)
How do we know which block of data is stored?
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)

## Slide 32: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
Access 4
0….01
0…………………….00
Miss
Data[1]
0…………… 00

## Slide 33: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
0
0
0
Valid
(1 bit)
1
1
Data[32769]

## Slide 34: Cache Operation
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT

## Slide 35: Alternative Placement
Assume 32 KByte cache with a 1 Byte cache block
Block 0
Block 1
Block 2
Block 32767
Address 0, 1, 2, 3, …..
Address 32678, ….
1 Byte = 8 bits
Use 15 MSBs of address to determine index
Consider following stream of accesses:
Addr 0, Addr 1, Addr 0, Addr 1,..
Bad Idea!