## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Caches
Instructor: Siddharth Garg

## Slide 2: Cache Organization
Caches store data in chunks of “cache blocks”
  Access to a cache returns an entire cache block
  A block can be as small as 1 byte, but can be larger (example: 4 bytes)
32 KB cache
1 Byte cache block
i.e., 32768 blocks
32 bit address
from CPU
Where does a block go when it is fetched into cache? (Placement)
How do we know if a block already exists in the cache? (Identification)
Which block should we kick out if there isn’t enough room? (Replacement)

## Slide 3: Direct Mapped Cache
Assume 32 KByte cache with a 1 Byte cache block
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
1 Byte = 8 bits

## Slide 4: Direct Mapped Cache: Placement
Each block in the cache has a log2(32768) = 15 bit “index”
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
Index
Index
(15 bits)
15 LSBs of address are used to look up (index) into the cache

## Slide 5: Direct Mapped Cache: Identification
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Addr 0
Addr 32768
0….00
0…………………….01
Addr ….
0….00
1…………………….11
Data Array
(8 bits)
How do we know which block of data is stored?
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)

## Slide 6: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
Access 4
0….01
0…………………….00
Miss
Data[32769]
0…………… 00

## Slide 7: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
0
0
0
Valid
(1 bit)
1
1
Data[32769]

## Slide 8: Cache Operation
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT

## Slide 9: Alternative Placement
Assume 32 KByte cache with a 1 Byte cache block
Block 0
Block 1
Block 2
Block 32767
Address 0, 1, 2, 3, …..
Address 32678, ….
1 Byte = 8 bits
Use 15 MSBs of address to determine index
Consider following stream of accesses:
Addr 0, Addr 1, Addr 0, Addr 1,..
“Conflict Misses”
Bad Idea!

## Slide 10: Set Associative Caches
Direct mapped caches can have miss rate due to conflicts
  Each address maps to a unique location in the cache
Assume addresses A and B with same index bits
  Sequence: A, B, A, B, A….. results in 100% cache miss rate!
Set-associative cache: each address can map to N different locations in the cache!
  “N-way” set associative cache
  2-way set associate cache has ~0% cache miss rate for sequence A, B, A, B …

## Slide 11: 2-Way Set Associative Cache
2-way set-associative 32 KB cache with 1 Byte blocks
Set 0
Data Array
(8 bits)
Tag Array
(? bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(? bits)
Set 1
Set 16383
Way 0
Way 1

## Slide 12: Placement
Set 0
Data Array
(8 bits)
Tag Array
(? bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(? bits)
Set 1
Set 16383
Way 0
Way 1
Index
(? bits)
Tag
(? bits)
Data mapped to a unique set but can be placed in either way
Index
(14 bits)
Tag
(18 bits)

## Slide 13: Identification
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
=
&
HIT?
=
&
HIT?

## Slide 14: Replacement
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
Where should C go?
(Addresses A, B, C map to same set)

## Slide 15: Least Recently Used (LRU)
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
Replace least recently used block
Data[C]
Tag[C]
Evicted!

## Slide 16: Implementing LRU
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
MRU
(1 bit)
0
1
0
LRU = NOT MRU

## Slide 17: Practical LRU Implementation
LRU is hard to implement in hardware for N>2
  Keep track of all possible N! orderings of N ways
  A linked list in which the head points to MRU and tail points to LRU
  Example: N=4; 4 x 2 bits = 8 bits per cache set and extra logic to update list on every access
Alternative policies that are more hardware friendly
  NOT MRU: same as LRU for N=2, requires only log(N) bits, easy update
  Hierarchical: for N=4, divide ways into 2 groups of 2 ways

## Slide 18: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | A | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 0 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?

## Slide 19: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | D | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 1 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?
Not the true LRU block!

## Slide 20: Exploiting Spatial Locality
Recall that if the byte from address i is accessed, then byte from address i+1 is likely to be accessed
  Pull in multiple contiguous bytes of data in each access
  Use larger block size!
Example: 32KB direct mapped cache with 8 Byte (64 bit) blocks
  i.e., cache has 4096 Byte blocks
Block 0
Block 4071
Data Array
(8 bytes)
Block 1
Index
(12 bits)
Offset
(3 bits)
Selects a byte from the block
Selects a block
Tag Array
(17 bits)
Tag 0
Tag 4095
Tag
(17 bits)
Valid

## Slide 21: Cache Operation
Block 0
Block 1
Block 2
Block 4095
Data Array
(8 bytes)
Tag 0
Tag 1
Tag 2
Tag 4095
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT
Index
(12 bits)
Offset
(3 bits)
Tag
(17 bits)
8 Bytes
8:1 MUX
1 Bytes

## Slide 22: Impact of Block Size
Sequence of addresses: A, A+1, A+2, A+3 …
  4 consecutive misses for 1 byte block size
  1 miss and 3 hits for 4 byte block size
Small block sizes don’t exploit any spatial locality
What happens if the block size increases for the same cache size
  Fewer number of larger blocks
[Source: D Brooks CS146 Lecs]

## Slide 23: In Class Exercise 1
Determine the number of offset bits, index bits and tag bits for a 4-way, 8KB cache with 8 Byte blocks. Assume that the cache is Byte addressable with a 32 bit address.
  Offset: 3 bits (8 byte blocks that are byte addressable)
  Number of sets: 213 bytes / ( 4 ways x 8 bytes per way) = : 213 bytes / 25 bytes = 28 sets
  Index: 8 bits
  Tag: 32 – 8 – 3 = 21 bits

## Slide 24: Write Policies
What should we do on a cache store/write access
  Cannot perform tag look-up and data-array lookup in parallel (why?)
  First access tag array and if there is a write hit, write to the data array
  Increases the delay of a cache access (recall: period is determined by the worst-case)
What do on a write hit?
  When there is a tag match (i.e., block exists in cache)
What to do on a write miss?
  When the data block is not in the cache?

## Slide 25: Write Hit Policies
When to propagate new (“dirty”) values to lower levels
  Write-back policy: lazy, take care of it later
  Write-through policy: update lower levels immediately
Write-back policy
  Modify the data in the current cache level only
  When to update the data in the lower level? When cache block is evicted
  Dirty bit per cache block to keep track of blocks that have been updated
Pros
  Write happens at speed of current cache level
  multiple writes to the same block result in only one write back to main memory
Cons
  Evictions take more time
  Data inconsistency between cache and lower levels

## Slide 26: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
0
0
Dirty
(1 bit)
D 0
D 1
0
Write Data
(8 bits)
1

## Slide 27: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
0
0
Dirty
(1 bit)
D 0
D 1
0
DISCARD DATA

## Slide 28: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
0
0
Dirty
(1 bit)
D 0
D 1
1
WRITE-BACK DATA

## Slide 29: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
0
0
Dirty
(1 bit)
D 0
D 1
1
Write Data
(8 bits)
1

## Slide 30: Write Hit Policies
When to propagate new (“dirty”) values to lower levels
  Write-back policy: lazy, take care of it later
  Write-through policy: update lower levels immediately
Write-Through policy
  Update lower levels of cache/memory on every write
  No need for a dirty bit in the cache
Pros
  Reduces complexity of cache (no dirty bit)
  Reads never cause write-backs
  Consistency across levels of memory hierarchy
Cons
  Increased write bandwidth (multiple writes to same block)
  Potentially Increased write latency (wait for write to propagate to lower levels?)

## Slide 31: Write Through Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
Write Data
(8 bits)
Write-Through to Lower Level
Update data in cache

## Slide 32: Write Through Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
DISCARD DATA

## Slide 33: Write Buffers

## Slide 34: Write Miss Policies
What to do if a write access misses in the cache
  Write allocate policy
  Write no-allocate policy
Write-allocate Policy
  Treat like a read miss, allocate block in cache for data
  Standard write hit actions follow
  Good match for write-back caches
Write no allocate Policy
  Do not allocate a cache block for the write, instead forward write to the next level
  This implies that only a read access will result in allocations
  Goes well with write through policy

## Slide 35: Summary of Write Policies
Write Policy | Hit/Miss | Where is Update Performed
Write Back, Allocate | Hit/Miss | L1
Write Back, No Allocate | Hit | 
Write Back, No Allocate | Miss | 
Write Through, Allocate | Hit/Miss | 
Write Through, No Allocate | Hit | 
Write Through, No Allocate | Miss | 
L1
L2
L1 and L2
L1+L2
L2